## Slide 1: Combustible Dust Training Program (C-DuST)
<number>
Notes: <number>

## Slide 2: Combustible Dust Training Program (C-DuST)
<number>
Grantee: Kirkwood Community College, Cedar Rapids, Iowa 52406-2068
Grantor: U.S. Department of Labor, Occupational Safety & Health Administration, Susan Harwood Training Grant Program Award Number: SH-17797-08-60-F-19
Project Title: Combustible Dust Training Program
(C-DuST)
Project Period: September 30, 2008 to September 30, 2009

## Slide 3: Disclaimer
This material was produced under grant number SH-17797-08-60-F-19 from the Occupational Safety and Health Administration (OSHA) of the U.S. Department of Labor. It does not necessarily reflect the view or policies of the U.S. Department of Labor, nor does mention of trade names, commercial products, or organizations imply endorsement by the U.S. Government. This training manual was produced by Kirkwood Community College, Cedar Rapids, Iowa.
The information in this power point presentation has been compiled from a variety of sources believed to be reliable and to represent the best current opinion on the subject. However, neither Kirkwood Community College nor its authors guarantee accuracy or completeness of any information contained in this publication, and neither Kirkwood Community College or its authors shall be responsible for any errors, omissions, or damages arising out of the use of this information. Additional safety measures may be required under particular circumstances.
<number>
Notes: <number>

## Slide 4: Overview
According to a study by the Chemical Safety Board, Dust explosions are a serious problem in American industry. Over the last 28 years there have been approximately 3,500 combustible dust explosions, 281 of these have been major incidents resulting in the deaths of 119 workers and another 718 workers sustained injuries.
There were 13 reported agricultural dust explosions in the United States in 2005 resulting in 2 fatalities and 11 injuries.
<number>

## Slide 5: Goal
To improve the safety of workers in environments where combustible dusts may be encountered by increasing employee awareness of this hazard and by demonstrating how the hazard can be recognized and addressed in their workplace.
<number>

## Slide 6: Enabling Learning Objectives
Identify the elements necessary for dust to explode.
Explain how to prevent dust from reaching combustible levels.
Describe the difference between primary and secondary dust explosions.
<number>

## Slide 7: Terminal Learning Objective
Program participants will understand:
Combustible dust danger in their industry.
The Dust, Fire, and Explosive Pentagon.
The methods to prevent or mitigate the effects of combustible dust explosion and resulting fire.
<number>

## Slide 8: Introduction
The first documented dust explosion occurred in a Turin, Italy, bakery in 1785.
  The explosion was caused by the ignition of flour dust by a lamp in a bakery storeroom.
  It lead to the realization that grain dust is a highly explosive substance that must be handled carefully.
<number>

## Slide 9: Introduction
A Chemical Safety Board Study Shows:
From 1996 to 2005, a total of 106 explosions resulted in 16 fatalities and 126 injuries, at an estimated cost of $162.8 million in damages to the facilities.
In 2005, there were 13 grain dust explosions reported in the US.
A RARE EVENT
But catastrophic when it happens!
<number>

## Slide 10: Background
Organic Dust Fires and Explosions:
  Massachusetts
  (3 killed, 9 injured)
  North Carolina
  (6 killed, 38 injured)
  Kentucky
  (7 killed, 37 injured
Metal Dust Fire and Explosion: Indiana
(1 killed,1 injured)
<number>
Notes: <number>

## Slide 11: Organic Dust Fire and Explosion Massachusetts
Caused a primary explosion in ducts containing heavy deposits of Phenol formaldehyde resin dust.
Resulted in
Fire in a foundry shell molding machine:
  a dust cloud from ledge dust deposits outside the ducts and
  an explosion in the plant area.
<number>
Notes: <number>

## Slide 12: Organic Dust Fire and Explosion Massachusetts
Causal factors
Housekeeping to control dust accumulations;
• Ventilation system design;
• Maintenance of ovens; and,
• Equipment safety devices.
<number>
Notes: <number>

## Slide 13: Organic Dust Fire and Explosion: North Carolina
A fire at the plant caused dust to be dispersed and explode in the ceiling space
6 were killed, 38 injured
Plant and nearby buildings were severely damaged
Combustible polyethylene dust accumulated above suspended ceilings at pharmaceutical plant
<number>
Notes: <number>

## Slide 14: Experience in the Grain Handling Industry
In the late 1970s, grain dust explosions left 59 people dead
and 49 injured.
<number>
Notes: <number>

## Slide 15: Experience in the Grain Handling Industry
In 1987, OSHA promulgated the Grain Handling Facilities
standard (29 CFR 1910.272) still in effect.
<number>
Notes: <number>

## Slide 16
<number>
Imperial Sugar Company, Port Wentworth GA. Explosion and Fire Feb. 7, 2008 13 Dead and Numerous serious injuries

## Slide 17
Dawson Creek Elevator Fire
<number>

## Slide 18: Dawson Creek Dust Explosion Williamsburg Iowa
<number>

## Slide 19: Dust Explosions
The additional dust dispersed into the air may cause one or more secondary explosions.
These can be far more destructive than a primary explosion
An initial (primary) explosion in
processing equipment or in an area
where fugitive dust has accumulated may
shake loose more accumulated dust,
Or damage a containment system
(such as a duct, vessel, or collector).
<number>
Notes: <number>

## Slide 20: CASCADING EXPLOSIONS
<number>

## Slide 21
Some event disturbs the settled dust into a cloud
Dust cloud is ignited and explodes
Dust explosion in a work area
Dust settles on flat surfaces
Dust
Adapted from CSB
<number>
Notes: <number>

## Slide 22
Dust collector venting flame jet
Dust explosion in equipment
<number>
Notes: <number>

## Slide 23
Dust explosion in equipment
With dispersal
and ignition of 2 kg dust
by the flame jet
Dust
Collector
Dust explosion in equipment
<number>
Notes: <number>

## Slide 24: A timeline
The following nine slides depict a timeline for a dust explosion and the results of that explosion.
Slides prepared by Joseph P. Howicz CSP, CFPS
Accident Prevention Corporation
W.W.W. safetyman.com
<number>

## Slide 25
Time, msec.
(Timing of actual events may vary)
0 25 50 75 100 125 150 175 200 225 250 300 325
Primary deflagration inside process equipment
A Dust Explosion Event
<number>
Notes: <number>

## Slide 26
Shock wave caused
by primary deflagration
Time, msec.
0 25 50 75 100 125 150 175 200 225 250 300 325
A Dust Explosion Event
<number>
Notes: <number>

## Slide 27
Time, msec.
0 25 50 75 100 125 150 175 200 225 250 300 325
Shock waves reflected by surfaces within the building cause accumulated dust to go into suspension
A Dust Explosion Event
<number>
Notes: <number>

## Slide 28
Time, msec.
0 25 50 75 100 125 150 175 200 225 250 300 325
Dust clouds thrown in the air by the shock waves
A Dust Explosion Event
<number>
Notes: <number>

## Slide 29
Time, msec.
0 25 50 75 100 125 150 175 200 225 250 300 325
Primary deflagration breaks out of the equipment enclosure - creating a source of ignition
A Dust Explosion Event
<number>
Notes: <number>

## Slide 30
Time, msec.
0 25 50 75 100 125 150 175 200 225 250 300 325
Secondary deflagration ignited
A Dust Explosion Event
<number>
Notes: <number>

## Slide 31
Time, msec.
0 25 50 75 100 125 150 175 200 225 250 300 325
Secondary Deflagration is propagated through the dust clouds
A Dust Explosion Event
<number>
Notes: <number>

## Slide 32
Time, msec.
0 25 50 75 100 125 150 175 200 225 250 300 325
Secondary deflagration bursts from the building
<number>
Notes: <number>

## Slide 33
Time, msec.
0 25 50 75 100 125 150 175 200 225 250 300 325
Collapsed building with remaining fires
A Dust Explosion Event
<number>
Notes: <number>

## Slide 34: Types of Dusts Involved in Explosions
<number>

## Slide 35: Required Conditions for an Explosion
The dust must be combustible and fine enough to be airborne.
The dust cloud must beat the Minimum Explosive Concentration (MEC) for that Particular dust.
There must be sufficient oxygen in the atmosphere to support and sustain combustion.
There must be a source of ignition.
The dust must be confined.
The dust must be dry.
Dust Particle
<number>

## Slide 36: Ignition Sources
<number>

## Slide 37: Explosive Limits
The Minimum Explosive Concentration (MEC) for grain dust, grain flour, or ground feed ingredients varies according to the particle size and energy:
  Smaller particles are more powerful
  Caloric value of the product
Corn starch is considered one of the more volatile and powerful grain products.
As the size of the particle decreases the risk of a deflagration or explosion increases.
<number>

## Slide 38: Dust Combustibility
Combustible dust per NFPA 654
Prior to 2006 - “Any finely divided solid material that is 420 microns or smaller in diameter (material passing a U.S. No. 40 Standard Sieve) and presents a fire or explosion hazard when dispersed and ignited in air.”
2006 Edition – A combustible particulate solid that presents a fire or deflagration hazard when suspended in air or some other oxidizing medium over a range of concentrations, regardless of particle size or shape.
<number>
Notes: <number>

## Slide 39: Facility Dust Hazard Assessment
Dyes
Coal
Metals (e.g., aluminum, chromium, iron, magnesium, and zinc)
Fossil fuel power generation
Combustible dust explosion hazard may exist in a variety of industries
Food (e.g., candy, starch, flour, feed)
Plastics
Wood
Rubber
Furniture
Textiles
Pesticides
Pharmaceuticals
<number>
Notes: <number>

## Slide 40: The Prevalence of Dust
Examples of materials that have historically caused dust explosions include:
  Cosmetics
  Coal
  Dyes
  Grain and other dry foods
  Metal
  Pharmaceuticals
  Plastic and rubber
  Printer toner
  Soaps
  Textiles
  Wood and paper
<number>

## Slide 41: Housekeeping
NFPA 654 and FM Global Data Sheet 7-76 are referenced.
Clean immediately whenever a dust layer of 1/32-inch thickness accumulates
  over a surface area of at least 5% of the floor area of the facility or any given room.
  not to exceed 1,000 ft2
Sampling coal dust
<number>
Notes: <number>

## Slide 42: Housekeeping
An idealized approach based on:
Uniformity of the dust layer
Bulk density of 75 lb/ ft3,
Dust concentration of 0.35oz/ ft3, and
Dust cloud height of 10 ft.
25 Ft
40 Ft
10 Ft
5% of 20,000 ft2 building
<number>
Notes: <number>

## Slide 43: Where Do Dust Explosions Occur?
Dust explosions, for grain, usually occur at transfer points as in bucket elevators or enclosed conveyors.
In 1997, 50 percent of primary explosions occurred in elevator legs.
Accumulation of dust in suspended ceilings
Cyclone collectors
Electrostatic collectors
Holding bins
<number>

## Slide 44
Dust Industries
Wheels melted in dust explosion and fire
<number>
Notes: <number>

## Slide 45
Corn Milling, Wet
Establishments primarily engaged in milling corn or sorghum grain (milo)
Electric Generation
Transmission, and/or distribution of electric energy
Flour and Other Grain Mill Products
Except rice
Industry With Dust
For exact description of SICs see: http://www.osha.gov/pls/imis/sicsearch.html?p_sic=3999&p_search=
<number>
Notes: <number>

## Slide 46
Reconstituted Wood Products
Hardboard, particleboard, insulation board, (and
many similar products)
Chemicals and Chemical Preparations
NOC fatty acids, essential oils, gelatin (except
vegetable), many other materials
Prepared Foods,
Various food items – dry, powdered foods
Electroplating,
Plating, Polishing, Anodizing, and Coloring (polishing and tumbling)
Industry with Dust
<number>
Notes: <number>

## Slide 47
Pharmaceutical Preparations
Wood Products,
Sawmills and Planing Mills,
Cane Sugar Refining
Beet Sugar manufacturing
Mechanical Rubber Goods
Molded, Extruded, and Lathe-Cut
Motor Vehicle Parts and Accessories – Numerous items including wheels and transmission housings
Industry with Dust
<number>
Notes: <number>

## Slide 48
Crop preparation for market except cotton gins (cleaning, shelling, delinting)
Dry bakery products – cookies, crackers, pretzels and similar
Flavoring extracts, syrups, powders and related
Fabric mills, broadwoven manmade fibers and silk (weaving fabrics >12 inches wide)
Fabric finishers, broadwoven manmade fibers and silk (includes napping, sueding, teaseling)
Industry with Dust
<number>
Notes: <number>

## Slide 49
Textile goods (many materials including waste,
kapok, felt, recovered fiber)
Millwork
Wood kitchen cabinets
Structural wood members
Prefabricated wood buildings and
components
Wood household furniture, except upholstered
Industry with Dust
<number>
Notes: <number>

## Slide 50
Window blinds and shades and drapery
hardware
Industrial inorganic chemicals
Plastics, synthetic resins, and
elastomers (nonvulcanizable)
Cellulosic manmade fibers
Soap and detergents, except specialty
cleaners
Paints, varnishes, lacquers, enamels, and
allied products
Industry with Dust
<number>
Notes: <number>

## Slide 51
Manufacturing industries NOC (includes
many products e.g.: matches; candles; lamp
shades; feathers; artificial trees and flowers)
Farm product warehousing and storage
Sanitary treatment facilities
Refuse systems
Scrap and waste materials
Plastic materials and basic forms and
shapes
Industry with Dust
<number>
Notes: <number>

## Slide 52: Explosion Safeguards
Fire prevention and protection
Housekeeping
Dust control
<number>

## Slide 53: Fire Prevention and Control
Policies, practices and procedures designed to keep the conditions necessary for a fire from coming together (explosive pentagon)
  Fuel (dust)
    Dust is dry
    Dust is at MEC
  Oxygen
  Ignition source
  Confined or enclosed space
  Mixing of fuel and oxygen Explosive Pentagon
<number>

## Slide 54: Fire Prevention and Control
Hot work permits
Lockout/tagout policies
Design specifications for storage of flammable materials
Severity reduction policies, practices and procedures designed to minimize the spread of fire
Emergency plans
Alarm systems
<number>

## Slide 55: Fire Prevention and Control
<number>
Portable fire extinguishers
Cleanup policies, practices and procedures designed to return the affected area to an operational level
First aid
Recharging portable extinguishers
Removal of debris to an appropriate waste site
Equipment and facility repair

## Slide 56: Housekeeping
A crucial key to the reduction of fires and explosions is housekeeping.
Housekeeping relates to hazards in addition to fires and explosions.
Research has shown that facilities that are well maintained experience fewer fires, explosions and other accidents.
<number>

## Slide 57: Dust Control
NFPA 654 – contains
comprehensive guidance
Some of its recommendations:
Minimize the escape of dust from process equipment or ventilation systems;(fugitive dust).
Use dust collection systems and filters.
Utilize surfaces that minimize dust accumulation and facilitate cleaning.
Spots are not raindrops
<number>
Notes: <number>

## Slide 58: Dust Control
Deadly Dust
?
NFPA 654 –
guidance
Provide access to all hidden areas to permit inspection.
Inspect for dust residues in open and hidden areas, at regular intervals.
Clean dust residues at regular intervals.
<number>
Notes: <number>

## Slide 59: Dust Control
NFPA 654
Use cleaning methods that do not generate dust clouds if ignition sources are present.
Only use vacuum cleaners approved for dust collection.
Class II
Div 1
Group EFG
HAZ LOC
HAZ LOC
<number>
Notes: <number>

## Slide 60: Fugitive Dust Control and Housekeeping
Dust Clouds
Surfaces shall be cleaned in a manner that minimizes the generation of dust clouds.
Vigorous sweeping or blowing down with steam or compressed air produces
dust clouds and shall be permitted only if the following requirements are met:
RETROACTIVE
<number>
Notes: <number>

## Slide 61: Fugitive Dust Control and Housekeeping
Area and equipment vacuumed prior to blow down.
Electrical power and other sources of ignition shut down or removed from the area.
Only low gauge pressure
(15 psi) steam or compressed air to be used.
No hot surfaces capable of igniting a dust cloud or layer.
RETROACTIVE
<number>
Notes: <number>

## Slide 62: Dust Control
NFPA 654
Locate relief valves away from dust hazard areas and
Develop and implement a hazardous dust
  Inspection,
  Testing,
  Housekeeping, and
  Written control program
(Written with established frequency and
methods).
Dust
Clean
Up
<number>
Notes: <number>

## Slide 63: Dust Control
Reducing dust accumulations is a major concern for facilities that produce dust.
A good housekeeping program depends upon a combination of methods to control dust.
The methods used in a given facility will depend upon the type of facility and the volume of organic material handled or produced.
<number>

## Slide 64: Dust Control Methods
Vacuums especially in areas where dust accumulation is constant due to the job task being performed.
Wash down procedures where hoses and water can be used to remove accumulated dust.
Choke feeds to control the flow of grain and grain dust.
Dust control systems such as filters or cyclones.
<number>

## Slide 65: Recognizing Dust Hazards
All employees should be trained in hazard recognition:
  Conduct general facility wide appraisals of dust explosion possibilities on a periodic basis.
  Conduct internal and external audits in order to identify potential explosion hazards.
  Encourage a preventative attitude among employees for dust explosions.
  Have employees and supervisors identify explosion hazards through JHAs.
  Pay particular attention to dust collection systems and other areas not in plain view during the assessment.
<number>

## Slide 66
<number>
U.S. Chemical Safety and Hazard Investigation Board Photo

## Slide 67
<number>
U.S. Chemical Safety and Hazard Investigation Board Photo

## Slide 68: Engineering Controls
Avoid the use of compressed air (blow down), and dry sweeping.
Conduct workforce training and education courses.
Limit and control potential ignition sources.
Ensure electrical service in combustible dust areas is appropriate for hazardous (Class II) locations.
<number>

## Slide 69: Engineering Controls
<number>
Follow National Fire Protection Association (NFPA) standard 654.
Ensure operations involving dusts have proper engineering design and controls.
Maintain an effective housekeeping program.
Establish and maintain a preventative maintenance program.
NFPA
654
Dust
Explosions
. . .

## Slide 70: Lessons Learned
West Pharmaceutical Services, Inc.
  On January 29, 2003, a massive dust explosion at the West Pharmaceutical Services facility in Kinston, North Carolina, killed six workers and destroyed the facility.
  The explosion involved a part of the building used to compound rubber.
    The compounding process produced a powder that was carried by air currents to the space above a suspended ceiling.
  Employees not trained on the hazards.
<number>

## Slide 71: West Pharmaceutical
<number>

## Slide 72: Lessons Learned
CTA Acoustics, Inc.
  On February 20, 2003, a series of dust explosions at the CTA Acoustics facility in Corbin, Kentucky, claimed the lives of seven workers, injured 37, and destroyed the manufacturing facility.
  This facility primarily made acoustic insulation for automobiles.
    A curing oven that had been left open because of a temperature control problem likely ignited the combustible resin dust stirred up by workers cleaning the area near the oven.
  Had CTA had adhered to NFPA 654 (2000) standards for housekeeping and fire/explosion barriers, the explosions could have been prevented or minimized.
<number>

## Slide 73: CTA Acoustics Inc.
<number>

## Slide 74: Lessons Learned
Hayes Lemmerz International.
  On October 29, 2003, aluminum dust exploded at the Hayes Lemmerz International facility in Huntington, Indiana, killed one worker and injured several others.
    This explosion involved equipment used to re-melt scrap aluminum
    The scrap aluminum was chopped into small chips, pneumatically conveyed to the scrap processing area, dried, and fed into a melt furnace .
      Transporting and drying the aluminum chips generated explosive aluminum dust, which was then pulled into a dust collector.
<number>

## Slide 75: Hayes Lemmerz International
<number>

## Slide 76: Lessons Learned
Safety Issues Neglected
  Facility management failed to conform to NFPA standards that would have prevented or reduced the effects of the explosions.
  Company personnel, government enforcement officials, insurance underwriters, and health and safety professionals inspecting the facilities failed to identify dust explosion hazards or recommend protective measures.
  The facilities contained unsafe accumulations of combustible dust and housekeeping was inadequate.
  Workers and managers were often unaware of dust explosion hazards.
<number>

## Slide 77: Lessons Learned
Safety Issues Neglected
  Procedures and training to eliminate or control combustible dust hazards were inadequate.
  Previous fires and other warning events were accepted as normal, and their causes were not identified and resolved.
  Dust collectors were inadequately designed or maintained to minimize explosions.
  Process changes were made without adequately reviewing them for potential hazards.
<number>

## Slide 78: Summary
Dust explosions are a serious problem in American industry.
During the past 25 years, at least 281 major combustible dust incidents were reported, that killed 119 and injured 718 workers, and destroyed many industrial facilities.
Facilities fail to follow the widely recognized standards of good engineering practice in the NFPA’s voluntary consensus standards.
<number>

## Slide 79: Summary
Facilities do not:
  Implement appropriate engineering controls
  Perform adequate maintenance
  Implement good housekeeping practices
  Follow other measures that could have prevented the explosions
  Provide adequate hazard recognition training for employees
  Establish overall safe work practices
<number>

## Slide 80
<number>