## Slide 1: EXTINGUISHER
Fire Safety & Fire Extinguisher Use
Notes: WELCOME STUDENTS.
INTRODUCE YOURSELF.
REMIND STUDENTS ABOUT:
  ATTENDANCE ROSTER.
  FEEDBACK FORM (IF USED).
  HANDOUTS (IF USED--COPIES OF SLIDES 8 AND 15).

## Slide 2: Objectives
Understand the combustion process and different fire classes
Understand fire extinguisher types, operating procedures
Understand basic firefighting concepts:
  R.A.C.E.
  P.A.S.S.
Fire Safety & Fire Extinguisher Use
Notes: BRIEFLY REVIEW OBJECTIVES.

## Slide 3: The Combustion Process
Fire Safety & Fire Extinguisher Use
Three components
Need all three components to start a fire
Fire extinguishers remove one or more of the components.
Notes: ASK “WHAT FOUR INGREDIENTS ARE NEEDED TO CREATE A FIRE?” AND SHOW SLIDE.
EXPLAIN HOW IT SHOWS “FIRE TETRAHEDRON”--FOUR-SIDED FIGURE SHOWING RELATIONSHIP BETWEEN COMPONENTS OF COMBUSTION PROCESS (UPDATE FROM OLD “FIRE TRIANGLE”--ADDS CHEMICAL CHAIN REACTION AS FOURTH ELEMENT).
EXPLAIN THAT EACH COMPONENT IS EQUALLY IMPORTANT.
ASK “HOW DO YOU PUT OUT A FIRE?” (REMOVE ONE OR MORE OF THE ABOVE ELEMENTS). EXPLAIN HOW EXTINGUISHERS WE USE ARE ALL DESIGNED TO DO THIS.

## Slide 4: Fire Classes
A Trash Wood Paper
C Electrical Equipment
B Liquids Grease
COMBUSTIBLE
METALS
D
wood
paper
cloth
etc.
gasoline
oil
grease
other solvents
computers
fax machine
other energized electrical equip.
magnesium
sodium
potassium
titanium
other flammable metals
Notes: DESCRIBE THE FIVE FIRE CLASSES ON THIS AND NEXT SLIDE.
POINT OUT OLD AND NEW FIRE SYMBOLS--USED TO MARK EXTINGUISHERS FOR SUITABILITY FOR USE ON FIRE CLASSES.
TO DECIDE IF EXTINGUISHER IS APPROPRIATE, MATCH SYMBOL TO TYPE OF FIRE BEING ENCOUNTERED.

## Slide 5: Fire Classes (cont.)
K Cooking Media
Recently recognized by NFPA 10
Fires involving combustible oils, lards and fats in commercial cooking.
CLASS K FIRES
Notes: RECENT ADDITION TO NFPA 10.
DESIGNED FOR USE WITH HOTTER BURNING NON-SATURATED FAT FIRES.

## Slide 6: Fire Extinguisher Anatomy
DISCHARGE HOSE
DISCHARGE NOZZLE
DISCHARGE ORIFICE
BODY
DATA PLATE
CARRYING
HANDLE
PRESSURE GAUGE
(not found on CO2
extinguishers)
DISCHARGE LEVER
DISCHARGE LOCKING PIN
AND SEAL
Notes: POINT OUT DIFFERENT COMPONENTS OF PORTABLE FIRE EXTINGUISHER.
POINT OUT THAT CO2 EXTINGUISHER IS UNIQUE IN THAT IT DOES NOT HAVE PRESSURE GAUGE.

## Slide 7: Fire Extinguisher Types
Class “A” fires only
2.5 gal. water (up to 1 minute discharge time)
Has pressure gauge to allow visual capacity check
30-40 ft. maximum effective range
Can be started and stopped as necessary
Extinguishes by cooling burning material below the ignition point.
PRESSURIZED WATER

## Slide 8: Fire Extinguisher Types (cont.)
Class “B” or “C” fires
2.5-100 lb. of CO2 (8-30 seconds discharge time)
Has NO pressure gauge--capacity verified by weight
3-8 ft. maximum effective range
Extinguishes by smothering burning materials
Effectiveness decreases as temperature of burning material increases.
CARBON DIOXIDE (CO2)

## Slide 9: Fire Extinguisher Types (cont.)
Class “A”, “B”, or “C” fires
2.5-20 lb. dry chemical (ammonium phosphate) 8-25 seconds discharge time)
Has pressure gauge to allow visual capacity check
5-20 ft. maximum effective range
Extinguishes by smothering burning materials.
MULTIPURPOSE DRY CHEMICAL

## Slide 10: Fire Extinguisher Summary
EXTINGUISHER TYPE
WORKS BY
EFFECTIVE AGAINST
PRESSURIZED WATER
CARBON DIOXIDE
MULTIPURPOSE DRY CHEMICAL
COOLING
SMOTHERING
SMOTHERING
Notes: BRIEFLY REVIEW EACH EXTINGUISHER TYPE, STRENGTHS, WEAKNESSES.
POINT OUT STUDENTS HAVE COPY OF THIS SLIDE AS ONE OF HANDOUTS.

## Slide 11: Fire Emergency Response
R
Rescue
Alarm
Contain
Extinguish
A
C
E
Notes: ASK “WHAT DO I DO IF I SEE A FIRE?”
RESCUE VICTIMS.
ALARM ACTIVATION TO SUMMON HELP.
CONTAIN FIRE TO PREVENT SPREAD--CLOSE DOORS, WINDOWS, SHUT OFF EXHAUST, ETC.
EXTINGUISH THE FLAMES--PUT THE FIRE OUT.

## Slide 12: Fighting the Fire
Pull the pin
Aim low at
the base of flames
Squeeze the handle
Sweep side to side
P
A
S
S
Notes: IF YOU DECIDE TO FIGHT FIRE, USE “P.A.S.S.” ACRONYM TO REMEMBER HOW TO OPERATE THE EXTINGUISHER PROPERLY.

## Slide 13: Firefighting Decision Criteria
Know department emergency procedures and evacuation routes
Know locations of extinguishers in your area and how to use them
Always sound the alarm regardless of fire size
Avoid smoky conditions
Ensure area is evacuated
Don’t attempt to fight unless:
  Alarm is sounded
  Fire is small and contained
  You have safe egress route (can be reached without exposure to fire)
  Available extinguishers are rated for size and type of fire
If in doubt, evacuate!
“DON’T ATTEMPT TO FIGHT UNLESS YOU ARE TRAINED”
Notes: ASK “HOW DO I DECIDE TO FIGHT THE FIRE OR EVACUATE?”
IF ONE OR MORE OF THE ABOVE CRITERIA AREN’T MET, BUG OUT!
IF YOU DO USE AN EXTINGUISHER, PLACE IT OUT OF SERVICE AND NOTIFY THE APPROPRIATE PERSON(S) SO IT CAN BE RECHARGED OR REPLACED.

## Slide 14: Summary
Combustion Process (Fire Triangle)
Class A, B, C, D, K fires
Types of portable fire extinguishers:
  Operating procedures
  Capabilities and limitations
Basic firefighting concepts: R.A.C.E.
P.A.S.S.
Fire Safety & Fire Extinguisher Use
Notes: BRIEFLY REVIEW COMBUSTION PROCESS, FIRE CLASSES, TYPES OF EXTINGUISHERS, AND THEIR LIMITATIONS (REMIND STUDENTS OF HANDOUTS).
REVIEW “R.A.C.E”, “P.A.S.S.” ACRONYMS.
ASK FOR QUESTIONS.
REMIND STUDENTS TO SIGN ROSTER.

## Slide 15: Quiz Question 1
Fire extinguisher marked with an A is used on:
A) oil fires
B) Electrical fires
C) paper material fires
D) none of the above

## Slide 16: Quiz Question 2
Fire extinguishers marked with a B can be used on:
A) Paper, trash
B) Oil or Grease
C) Electrical
D) Non of the above

## Slide 17: Quiz addendum
How else you can kill a grease fire?
Smother
Baking Soda
A&B

## Slide 18: Quiz Question 3
Fire extinguisher marked ABC can be used on:
A) Wood, Paper
B) Electrical
C) Liquids and grease
D) All of the above

## Slide 19: Quiz Question 4
Fire Extinguishers marked with D are used for
A) Combustible chemicals
B) Magnesium
C) Potassium
D) other flammable metals
E) all of the above

## Slide 20: Quiz Question 5
For what fires is a Halon Fire Extinguisher being used?
Guess 1
Guess 2
Guess 3
Guess 4

## Slide 21: Halon
Halon fire extinguisher is important device to have, especially for emergency situations. It contains a gas that interrupts the chemical reaction that takes place when fuels burn. Halon fire extinguisher is often used to protect valuable electrical equipment since they leave no residue.
Such on expensive computers, server rooms, etc.
Since Halon manufacturing was banned, a hunt has been on for something that works as well. According to the Halon Alternatives Research Corp., more than 20 different kinds of alternatives exist as direct replacements.
Halon Replacement
  Those categories are inert gases and halocarbon compounds.