## Slide 1
Notes: <number>

## Slide 2: Overhead Crane Safety and Inspection Requirements
Notes: <number>

## Slide 3: Notice
It is the responsibility of the owner/user to install, inspect, test, maintain and operate a crane or associated lifting equipment in accordance with the applicable volume of the ANSI/ASME B30 Safety Standard, OSHA Regulations, ANSI-NFPA 70, National Electric Code, and local regulations and laws. If the crane or associated lifting equipment is installed as part of a total lifting system, it is also the responsibility of the owner/user to comply with the applicable ANSI/ASME B30 volumes that address other types of equipment used in the system. Further, it is the responsibility of the owner/user to require all personnel who install, inspect, test, maintain and operate a crane or associated lifting equipment to read and to comply with the contents of the instruction manuals furnished by the manufacturer of the crane or associated lifting equipment, and the applicable portions of the volume of the ANSI/ASME B30 Safety Standard, OSHA Regulations, ANSI/NFPA 70 and National Electric Code. If the crane or associated lifting equipment is installed as part of a total lifting system, the applicable ANSI/ASME B30 volumes that address other types of equipment used in the system must also be read and followed by all personnel.
Notes: <number>

## Slide 4: Daily Operator Inspection Requirements
  Daily inspections should be performed at the beginning of each shift or before initial use of the crane each shift by the operator or appointed person.
Notes: <number>

## Slide 5: Daily Operator Inspection Requirements
  Make sure crane or hoist is not tagged out. If a tag is in place, it is usually located at the power disconnect to the runway or on the pushbutton station.
  Check the load block to make sure all sheaves are running freely and sheave covers/guards are in place.
Notes: <number>

## Slide 6: Daily Operator Inspection Requirements
  Inspect the hook for the following:
    Is the safety latch in place? Does it operate correctly?
    Is the hook bent or twisted? The twist cannot exceed 10° from the plane of the unbent hook or as recommended by the manufacturer.
    Has the throat opening increased? The throat opening cannot increase by more than 15% or as recommended by manufacturer.
    Check the bowl conditions. Are there any gauges, nicks or cuts that could damage synthetic slings and etc.?
    Check the rotation of the hook. Does it rotate freely the whole 360°?
Notes: <number>

## Slide 7: Daily Operator Inspection Requirements
  Inspect the wire rope to make sure it is lubricated and that none of the following conditions exist:
    No kinks
    No broken or cut strands
    No bird caging
    No corrosion
    No core protrusion
    No crushed sections of rope
1.
2.
3.
  6.
Notes: <number>

## Slide 8: Daily Operator Inspection Requirements
  Inspect the control device to make sure all warning labels are in place and there are no cracks or missing bolts in the case.
Notes: <number>

## Slide 9: Daily Operator Inspection Requirements
  Inspect the system conditions
    Visually inspect the runway system. Are all bolts in place? Are there any obstructions on the runway?
    Visually inspect bridge, trolley and hoist connections. Does everything appear normal?
    Visually inspect the mainline conductor bar system. Are the conductors aligned properly? Are all joint covers in place? Are there any broken or loose support brackets?
Notes: <number>

## Slide 10: Daily Operator Inspection Requirements
  Check Operational Functions
    Does the “E” stop function correctly?
    Do all the directional buttons and motions function correctly?
    Test the hoist limit switches and any travel limit switches, if present, to ensure they are operating correctly. This should be done without load.
    If there are any horns or lights present, do they function properly?
    Do all motions of travel run smoothly with no unusual sounds present?
    Check the ground for any signs of oil leakage.
    Pick up a load and make sure the brakes are functioning properly.
Notes: <number>

## Slide 11: Daily Operator Inspection Requirements
  If any damage or malfunctions are noted during the daily inspection, the operator shall immediately advise the appointed person so corrective action can be taken.
  If a malfunction occurs during operation, the operator shall immediately advise the appointed person so corrective action can be taken.
  If corrective action has not been completed by the end of the shift, the operator will advise the operator or operators of the next shift that corrective action is required and verify the crane is tagged out with an out of order sign.
Notes: <number>

## Slide 12: Periodic Inspection
In addition to daily inspections, OSHA also requires periodic inspections of overhead cranes. The definition and frequency of periodic inspections are defined in the coming slides.
Notes: <number>

## Slide 13: Periodic Inspection
A periodic inspection is a detailed visual and operational inspection whereby individual components are examined to determine their condition. The periodic inspection is performed as often as quarterly and is based on service, environmental and application factors as determined by a qualified person or as outlined in the following table.
Notes: <number>

## Slide 14: Periodic Inspection Chart (as required by OSHA)
Notes: <number>

## Slide 15: Periodic Inspection Items
  Structural Members
  Signs and Labels
  Connection Points
  Sheaves and Drums
  Shafts, Axles, Wheels, Couplings
  Brakes (holding and control)
  Indicators, Gauges
  Self-Contained Electric, Hydraulic, or Gasoline Powered Generating Units
  Transmissions
  Electrical Components
  Covers and Guards
  Bumpers and End Stops
  Trolley and Runway Rail
  Runway Structure
  Conductor System
  Below-the-Hook Devices
Notes: <number>

## Slide 16: Periodic Inspection Items
Structural members, such as girders, end trucks, footwalks, trap doors, ladders, handrails, trolley frame, cab, etc.
  Check for deformed, cracked, corroded or unsecured members. Are foot walks free of debris, grease, etc.?
  Does cab have a fire extinguisher. Is it the proper type?
Notes: <number>

## Slide 17: Periodic Inspection Items
Signs and Labels
  Check for proper capacity labels. Are they legible from the floor? Are warning signs in place and legible?
  Were cranes load tested? Did you record this in your records? All new cranes must be load tested after installation.
Notes: <number>

## Slide 18: Periodic Inspection Items
Connection Points
  Check for loose/broken bolts or rivets. Check for cracked or insufficient welds.
Notes: <number>

## Slide 19: Periodic Inspection Items
Sheaves and Drums
  Check for worn grooves, worn groove lands, sharp edges and cracks.
Notes: <number>

## Slide 20: Periodic Inspection Items
Shafts, Axles, Wheels, Couplings
  Check for worn, cracked, bent or broken parts. Check for loose/missing hardware.
Notes: <number>

## Slide 21: Periodic Inspection Items
Brakes (Holding and Control)
  Check for excessive wear and proper adjustment on brake system parts, linings, pawls and ratchets. Check for proper functioning of electric control brake.
Notes: <number>

## Slide 22: Periodic Inspection Items
Indicators, Gauges or Other Devices
  Check for load, wind and other indicators over their full range. Re-calibrate as required.
Notes: <number>

## Slide 23: Periodic Inspection Items
Transmissions
  Check for excessive wear of chain drive sprockets and excessive chain stretch. Open gearbox inspection covers and check for gear teeth wear and proper lubrication.
Notes: <number>

## Slide 24: Periodic Inspection Items
Electrical Components
  Check all electrical apparatuses for signs of pitting or any deterioration of controller contactors, limit switches, pushbutton stations, motor slip rings, brushes or resistors.
  Check for any loose wire connections for damaged wiring.
  Check for evidence of overheating.
  Make sure the door or cover is closed properly.
Notes: <number>

## Slide 25: Periodic Inspection Items
Electrical Components
  Controller contactors
  Limit switches
  Push button stations
Notes: <number>

## Slide 26: Periodic Inspection Items
Electrical Components
  Motor slip rings
  Brushes
  Resistors
Notes: <number>

## Slide 27: Periodic Inspection Items
Covers and Guards
  Check that all covers or guards are in place, secure and undamaged.
Notes: <number>

## Slide 28: Periodic Inspection Items
Bumpers and End Stops
  Check all bumpers and end stops for damage. Check for proper restraints and obvious undersizing or improper energy absorption capabilities.
Notes: <number>

## Slide 29: Periodic Inspection Items
Trolley and Runway Rail
  Check rails and fastening devices for looseness, gaps, misalignment or wear.
Notes: <number>

## Slide 30: Periodic Inspection Items
Trolley and Runway Rail
Notes: <number>

## Slide 31: Periodic Inspection Items
Runway Structure
  Check runway structure for proper anchors, loose bolted connections, corrosion, cracked or deformed members.
Notes: <number>

## Slide 32: Periodic Inspection Items
Conductor System
  Check the conductor systems for:
    Alignment
    Fastening
    Splices
    Power feeds
    Conductor shoes for wear
Notes: <number>

## Slide 33: Periodic Inspection Items
Below-the-Hook Devices
  Check for cracks or structural damage. Check mechanical components for wear, alignment and missing/loose hardware. Check all motors, controls and wiring. Check that all guards are in place and secure.
Notes: <number>

## Slide 34: Operational Safety
Do not overload the crane or hoist. Make sure the combined weight of the lifter and load does not exceed the rated load capacity of the crane or hoist.
Refuse to make lift if you are unsure of any issues. Do not proceed until all issues are resolved.
Notes: <number>

## Slide 35: Operational Safety
Take instructions only from the person designated to give signals.
Do not ride or allow other people to do so.
Notes: <number>

## Slide 36: Operational Safety
To pick up a load, move the crane and hoist/hook directly above the load to eliminate the possibility of side loading and minimize load swing.
Notes: <number>

## Slide 37: Operational Safety
Before lifting, ensure that everyone is clear of any pinch or crush zones.
When starting to lift the load, only lift it a few inches off the ground to verify hoist brake is functioning properly before continuing with the lift.
Notes: <number>

## Slide 38: Operational Safety
Make sure the rigging is in good condition and that safe rigging practices are applied.
Ensure rigging is appropriate for the load size, shape and weight.
Notes: <number>

## Slide 39: Operational Safety
Always maintain a clear view of the crane path so you can observe any obstacles or personnel in your path.
Notes: <number>

## Slide 40: Operational Safety
Use one continuous motion when traveling. Try not to start/stop (plug) as this will result in load swing.
Notes: <number>

## Slide 41: Operational Safety – Moving a Load
Do not lift loads over people. Stay out from under the load and make sure other people remain at a distance.
Do not become distracted while traveling. If you need to speak with someone, cease operation of the crane.
Notes: <number>

## Slide 42: Operational Safety
Never leave a suspended load unattended. If you must leave the area, lower the load to the ground before doing so.
Notes: <number>

## Slide 43: Operational Safety – Moving a Load
Stay clear while moving a load. Do not allow the load to swing. Use a rod to push the load or a tag line to pull the load. Exercise particular caution with sheet lifters. Be sure to keep the load level. Tilting the lifter could cause the load to slide off the lifter.
Notes: <number>

## Slide 44: Operational Safety
When the crane is not in use, always raise the crane hook above head level.
Notes: <number>

## Slide 45: Recommended Forms
  Maintenance Log
  Frequent Daily Check List
  OSHA Crane Inspection Report
  Operator Training Questionnaire
Notes: <number>

## Slide 46: Recommended Forms
Maintenance Log. Click on the picture to open PDF file.
Notes: <number>

## Slide 47: Recommended Forms
Daily Inspection Report. Click on the picture to open PDF file.
Notes: <number>

## Slide 48: Recommended Forms
OSHA Crane Inspection Report. Click on the picture to open PDF file.
Notes: <number>

## Slide 49: Recommended Forms
Operator Training Questionnaire. Click on the picture to open PDF file.
Notes: <number>

## Slide 50: Standard Hand Signals
Notes: <number>

## Slide 51: Standard Hand Signals
Notes: <number>

## Slide 52: Standard Hand Signals
Notes: <number>