## Slide 1: Silicosis Prevention
Introduction to OSHA’s Special Emphasis Program

## Slide 2: Silica Special Emphasis Program
Began in 1997
Part of OSHA current Strategic Plan (through 2008)
Compliance Enforcement
Consultation
Training and Outreach
  OSHA Web-site
Standard Development and Stakeholders Meetings Currently in Progress

## Slide 3: Why Target Crystalline Silica Exposure?
1. Toxicity is well documented
2. Widespread worker overexposure
3. Exposures can be controlled

## Slide 4: Case Study, 1930’s: Hawk’s Nest Tunnel
Gauley Mt., W. VA.
1930 – 1935
Estimated Deaths from Silicosis:
  500 to 750

## Slide 5: Progress made: Exposures in the 21st Century

## Slide 11: What is Silica?
Composes 15% of Earth’s Crust
1. Crystalline Silica (regulated)
  has a diagnostic X-ray diffraction pattern
2. Amorphous Silica (not regulated)
  “without form”
  cannot distinguish by X-ray diffraction
  Glass is common example

## Slide 12: Crystalline Silica
Examples:
  Sand, Granite, other “Hard” rocks
Quartz, most common
Cristobalite, Tridymite
    Much less common, but more toxic than quartz

## Slide 13: Potential Silica Exposures
Foundries
Ceramics Industry
Abrasive Blasting
Construction
Manufacturing of cleaning agents
Mining Operations
Use of Coal (e.g., electric power generation)

## Slide 14: Silica and Mortality
250 Worker deaths per year from Silica
  (Compare to 175 deaths/yr from trenching accidents)
Silicosis
Tuberculosis
Heart Disease
Lung Cancer?
  Suspect Hum. Carcinogen –A2 (ACGIH)

## Slide 15: Health Effects
Chronic-Obstructive Pulmonary (Lung) Disease--COPD
Affects Aveolar Surface
  Decreases Elasticity
  Prevents Oxygen/CO2 Exchange

## Slide 17: Silicosis Diagnosis
Requires Chest X-ray
X-ray must be read by qualified “B-Reader”
Silica Nodules are Non-Reversible

## Slide 19: Disease Classes of Silicosis
1. Acute Silicosis (Highest Exp.)
  Latency of weeks to 5 years
2. Accelerated Silicosis (High Exp.)
  Latency of 5 to 15 years
3. Chronic Silicosis (Moderate Exp.)
  Latency >15 years

## Slide 20: Silicosis: Non-Curable Disease
Prevention through Safe Workpractice is critical

## Slide 21: Silicosis Prevention Program
Engineering Control of Dust
Training on crystalline silica
Respiratory protection program
Work clothes, change and wash area

## Slide 22: Silicosis Prevention Program
Air monitoring program
Medical surveillance
Housekeeping and Regulated Areas
Recordkeeping