## Slide 1: Welding, Cutting, and Brazing
MODULE 16

## Slide 2: Hazards of Welding Operations
Fire hazards
Metal splatter
Electric shock
Explosion hazards
Released gases
Radiant energy
Where would these hazards be found on oil and gas well sites?

## Slide 3: Three Basic Types of Welding
Gas – Slower and easier to control than electric arc. Uses gas flame over metals until molten puddle is formed. Most popular fuels used with oxygen include acetylene, mapp gas, and hydrogen.
Arc – Two metals are joined by generating an electric arc between a covered metal electrode and the base metal.
Oxygen and Arc Cutting – Metal cutting in welding is the severing or removal of metal by a flame or arc.

## Slide 4: Oxygen and arc cutting
Most common cutting processes :
  Oxygen Cutting: Metal is heated by gas flame and an oxygen jet does the cutting.
  Arc Cutting: Intense heat of electric arc melts away the metal.

## Slide 5: Regulations
29 CFR 1910 Subpart Q
  General Industry
29 CFR 1926 Subpart J
  Construction
API RP 54 Section 20
  Hotwork, Welding, and Flame Cutting Operations

## Slide 6: General Requirements
29 CFR 1910.252

## Slide 7: Fire Prevention Safeguards
Fire Hazards should be removed if the welded object cannot be readily moved.
Guards should be used if removing fire hazards is not possible.
Restrictions apply (no cutting or welding allowed) if none of the above is possible.

## Slide 8: Subtitles & Transitions
FOR EXAMPLE…

## Slide 9: Special Precautions
Protect nearby combustible materials from sparks that might escape through openings in floors or walls.
Fire Extinguishers must be ready for instant use.
Fire Watch lasting at least 30 min after welding or cutting operations is required if more than a minor fire might develop and if certain combustible materials are present.

## Slide 10: Special Precautions
Authorization: A responsible individual must inspect the area and designate precautions, preferably by written permit.
Floors: Combustible materials must be swept 35 feet away; combustible floors must be wetted or protected (while preventing arc welding shock)

## Slide 11: Special Precautions
Prohibited areas for welding:
  Unauthorized by management
  Where sprinklers are impaired
  Explosive atmospheres
  Near storage of large quantities of readily ignitable materials
Relocation of Combustibles: Combustibles shall be moved 35 feet away or properly protected or shielded.

## Slide 12: Special Precautions
Ducts: Ducts & conveyor systems that might carry sparks must be shut down.
Combustible walls must be shielded or guarded.
Noncombustible walls, partitions or ceilings (when welded) require opposite-side moving of combustibles or a fire watch.
Combustible cover: No welding on certain metal building components having combustible covers or layers.

## Slide 13: Special Precautions
Pipes (or any metal) close enough to combustibles to cause ignition by conduction may not be cut or welded.
Management responsibilities:
  Establish proper areas and procedures
  Designate responsible individual
  Ensure training
  Advise contractors of hazards

## Slide 14: Special Precautions
Supervisor responsibilities:
  Safety of equipment & procedures
  Determine combustibles & hazardous areas
  Protect combustibles from ignition through moving, shielding and scheduling
  Secure authorizations
  Give go-ahead to cutter or welder
  Ensure fire protection
  Ensure fire watches if required

## Slide 15: Welding or Cutting Containers
Used containers must be cleaned of flammable materials or other materials that could release toxic of flammable vapors when heated.
Venting & purging is required for hollow spaces or cavities.

## Slide 16: Confined Spaces
Precautions must be taken during long* pauses in arc welding to prevent
  accidental contact of electrodes
  torch valve gas leaks in gas welding.
*During lunch or overnight

## Slide 17: Protection of Personnel
Railing or other suitable fall protection must be provided as required.
Welding cable and other equipment must be kept clear of passageways, ladders and stairways.
Eye protection and protective equipment of specific appropriate types must be worn. Nearby workers must be protected from arc welding rays.

## Slide 18: Subtitles & Transitions
FOR EXAMPLE…

## Slide 19: Protection of Personnel
Work in confined spaces requires consideration of:
  Ventilation
  Securing cylinders and machinery
  Lifelines
  Electrode removal (arc welding)
  Gas cylinder shutoff (gas welding & cutting)
  Warning signs for hot metal

## Slide 20: Health Protection & Ventilation
General requirements for protecting welders are based on 3 factors:
  Dimensions of space (especially ceiling height) in which welding is to be done
  Number of welders
  Possible evolution of hazardous fumes, gases, or dust according to the metals involved.

## Slide 21: Natural and Mechanical Ventilation
Must not be restricted by screens
Sufficient to keep concentrations <PEL
Mechanical ventilation required for:
  Metals not described here
  Spaces <10,000 feet per welder
  Rooms with ceilings lower than 16 feet
  Confined spaces or areas with barriers to natural cross ventilation

## Slide 22: Dilution Ventilation
Contaminant should travel away from breathing zone.
Local exhaust ventilation may be more effective.
Poor
Fair
Good
Best

## Slide 23: Ventilation
Confined space: ventilation first; respirators if ventilation impossible
Specific rules for specific chemicals
Outdoors: Just stay below PEL

## Slide 24: Transmission pipeline
Special rules in 1910.252(d)(1)
  Special electric shock protection for wet conditions
  Pressure testing: Worker and public protection against blowing out or loose dirt
  Construction: API Std. 1104-1968
  Flammable substance lines: API Std. PSD No. 2201-1963
  X-ray inspection: ANSI Z54.1-1963

## Slide 25: Oxygen-Fuel Gas Welding & Cutting
General Requirements
  Flammable mixtures of fuel gases and air or oxygen must be guarded against.
  Maximum pressures of 15 psi for acetylene must be observed (with certain rare exceptions).
  Approved apparatus.
  Competent personnel in charge of supply equipment

## Slide 26: Cylinders & Containers
Approval & Marking:
  DOT compliant
  Legibly marked
  ANSI compliant connections
  Valve protection

## Slide 27: Cylinders & Containers: Storage
Away from heat sources (such as radiators)
When inside buildings:
  Well-protected, ventilated, dry location at least 20 ft from combustibles
  Assigned storage spaces, protected from damage & tampering
When empty: closed valves
When not in use: hand-tight valve protection caps

## Slide 28: Oxygen Storage
Protect oxygen cylinders from fire hazards such as acetylene:
Distance: 20 ft from fuel-gas cylinders or combustibles, or
Barrier: 5 ft high noncombustible partition with half-hour fire-resistance rating

## Slide 29: Arc Welding & Cutting
Use compliant equipment
Special design for exposure to weather, flammable gases, marine conditions…
Workmen who operate or maintain arc welding equipment shall be acquainted with the requirements of 1910.254 and 1910.252

## Slide 30: Arc Welding & Cutting
Electrode holders when not in use must be kept from shocking people and objects.
Protect against electric shock:
  Never use cables with splices within 10 feet (3 m) of the holder
  The welder should not coil or loop welding electrode cable around parts of his body
Maintenance must ensure safety:
  Damaged cables & equipment must be replaced.
  Work and cables must be joined properly and have adequate insulation.

## Slide 31: Operating procedures
Cylinders, cylinder valves, couplings, regulators, hose, and apparatus kept free from oily or greasy substances
Oxygen cylinders shall not be handled with oily hands or gloves
A jet of oxygen must never be permitted to strike an oily surface, greasy clothes, or enter a fuel oil or other storage tank

## Slide 32: Operating procedures
When transporting cylinders by a crane:
Use a cradle or suitable platform
Never use slings or electric magnets
Valve-protection caps always in place

## Slide 33: Operating procedures
Never use valve-protection caps to lift cylinders from one vertical position to another
Never use bars under valves or valve-protection caps to pry cylinders loose
  may use warm (not boiling) water

## Slide 34: Operating procedures
Before cylinders are moved:
Regulators shall be removed
Valve-protection caps, when provided for, shall be put in place
Unless cylinders are secured on a special truck

## Slide 35: Operating procedures
Cylinders without fixed hand wheels shall have keys, handles, or nonadjustable wrenches on valve stems while cylinders are in service

## Slide 36: Operating procedures
Fuel-gas cylinders shall be placed with valve end up whenever they are in use
Liquefied gases shall be stored and shipped with the valve end up

## Slide 37: Operating procedures
Before connecting a regulator to a cylinder valve:
  Open the valve slightly; close immediately
Open the valve while standing to one side of the outlet; never in front of it
Never crack a fuel-gas cylinder valve near other welding work or near sparks, flame, or other possible sources of ignition

## Slide 38: Operating procedures
Always open the cylinder valve slowly
Never open an acetylene cylinder valve more than 1.5 turns of the spindle, and preferably no more than 3/4 of a turn

## Slide 39: Hose and hose connections
Replace hose with leaks, burns, worn places, defects
When parallel lengths of oxygen and fuel hose are taped together, not more than 4 of 12 inches covered by tape

## Slide 40
Test Your Knowledge
How long must a fire watch continue?
A radius of 35 feet.
How far away must combustible materials be kept from welding?
Who is responsible for making fire watchers available?
During work in confined spaces, what must be left outside?
Gas cylinders & welding machines.
Supervisor.
At least 30 minutes.

## Slide 41: Examples & Diagnosis

## Slide 42: Subtitles & Transitions
FOR EXAMPLE…

## Slide 43: Subtitles & Transitions
FOR EXAMPLE…

## Slide 44: Subtitles & Transitions
FOR EXAMPLE…

## Slide 45: Subtitles & Transitions
FOR EXAMPLE…

## Slide 46: Subtitles & Transitions
FOR EXAMPLE…

## Slide 47: Subtitles & Transitions
FOR EXAMPLE…

## Slide 48: Subtitles & Transitions
FOR EXAMPLE…

## Slide 49: Subtitles & Transitions
FOR EXAMPLE…