## Slide 1
Ladder Safety
Environmental Health & Safety

## Slide 2: Ladder Safety - Introduction
Indispensable tools
Many sizes, shapes
Oregon: 500 workers injured annually
Most injuries: fall of less than 10 feet
Notes: Ladders are indispensable tools. We take them for granted in our day-to-day work and use them extensively in virtually all industries. Though they come in many sizes, shapes, and styles, they all serve the same purpose: to help us move vertically. They’re simply built and easy to use, but they’re not always user friendly. Each year in Oregon, about 500 workers are seriously injured when they fall from ladders. You don’t have to fall far to get hurt; most workers injured in falls from ladders are less than 10 feet above the ladder’s base of support.

## Slide 3: Ladder Safety - Introduction
Why?
Most falls involve portable ladders
  Move, tilt, shift during climbing
  Unstable/slippery base surfaces
  Misstep/slip of foot
  Loss of balance (overreach)
  Struck by vehicle
Notes: Why do people fall from ladders if they’re so easy to use? In general, most ladder falls involve portable ladders that move, tilt, or shift while a worker is climbing or descending. Unstable or slippery base surfaces are the primary reasons ladders fail. Other reasons include a misstep or a slip of the foot, loss of balance, an overreach, and being struck by a vehicle or other object.

## Slide 4: Ladder Safety - Introduction
To reduce ladder fall risks:
  Frequently inspect and maintain ladders
  Match tasks to appropriate ladders
  Set up ladders correctly
  Climb and descend ladders properly.
Employers - responsibility to train workers
Notes: Workers can reduce ladder fall risks by doing the following:
  Frequently inspect and maintain ladders
  Match tasks to appropriate ladders
  Set up ladders correctly
  Climb and descend ladders properly.
Employers, too, have a responsibility for training workers so they understand these safe work practices and can use them effectively.

## Slide 5: Ladder Safety - Introduction
OR-OSHA regulations
Division | Subdivision
2 (General) | D - Walking/ working Surfaces
3 (Construction) | X - Stairways and Ladders
4 (Agriculture) | D - Ladders and Scaffolds
Notes: This guide promotes safe work practices for portable ladders. You are encouraged to use it as a basic reference, but it does not replace OR-OSHA requirements for portable ladders, as shown in the table below.
Safety requirements for portable ladders
Division 2, subdivision D – walking/working surfaces, subparagraph 437-002-0026
Division 3, subdivision X - Stairways and Ladders , subparagraph 1926.1053 & 437-003-0065
Division 2, subdivision D - Ladders and Scaffolds , subparagraph 437-004-0340 - 437-004-0370

## Slide 6: Ladder Ratings
4 ratings
Based on maximum working load
Rating | Working Load
Extra heavy duty (I-A) | 300 pounds
Heavy duty (I) | 250 pounds
Medium duty (II) | 225 pounds
Light duty (III) | 200 pounds
Notes: There are many types of portable ladders, but they all receive one of four ratings, based on their maximum working load (the maximum weight they can safely support). Before you use a ladder, check its rating. And be sure not to subject it to a load greater than its rated capacity. The ratings:

## Slide 7: Types of Portable Ladders
Non-self-supporting ladders
  Two types
Self-supporting ladders
  5 types
Notes: Workers climb up or down to do all sorts of tasks, so it’s not surprising that ladders come in different types to help them accomplish those tasks. Portable ladders are either non-self-supporting (such as the straight ladder) or self-supporting (such as the standard step ladder). Within one of these two categories, you’re likely to find the right size, shape, and type of ladder to accomplish your task.

## Slide 8: Non-self-supporting ladders
Single portable or straight ladder
  Slip-resistant feet
  30 foot maximum length
  One worker
  Wood, metal, fiberglass
Notes: The single portable or straight ladder is indispensable for general use. It’s the most common type of portable ladder and has the widest range of applications.
When used on slippery surfaces, this ladder must have slip-resistant feet or be secured to prevent it from sliding. Rubber or neoprene ladder shoes are recommended for smooth, dry surfaces, and spikes are recommended for snow or ice.
Single portable ladders must not be longer than 30 feet and are intended for use by only one worker at a time. Such ladders are available in wood, metal, and reinforced fiberglass.

## Slide 9: Non-self-supporting ladders
Extension or section ladder
  Two or more sections
  Upper section on top
  Minimum section overlap
  Wood, metal, fiberglass
  One person
Notes: Extension ladders offer the greatest length in a general purpose ladder. The ladder consists of two or more sections that travel in guides or brackets, allowing adjustable lengths. The sections must be assembled so that the sliding upper section is on top of the lower section. Each section must overlap its adjacent section a minimum distance, based on the ladder’s overall length. The overall length is determined by the lengths of the individual sections, measured along the side rails. The table below shows the minimum overlap for ladders up to 60 feet long.

## Slide 10: Non-self-supporting ladders
Extension or section ladder
  Maximum length of ladder 72 feet
  Wood ladder < 60 feet
  Individual sections < 30 feet
  Non-slip base – tie off top
Ladder Length | Overlap
Up to and including 36 feet | 3 feet
Over 36 through 48 feet | 4 feet
Over 48 through 60 feet | 5 feet
Install positive stops on individual ladder sections to ensure required overlap. | 
Notes: Extension ladders are made of wood, metal, or reinforced fiberglass. Wood ladders can’t have more than two sections and must not exceed 60 feet. Metal and fiberglass ladders can have as many as three sections; however, the overall length must not exceed 72 feet. Individual sections of any extension ladder must not be longer than 30 feet. Extension ladders are for use by only one person at a time.
Make sure extension ladders have nonslip bases if there’s a chance the ladder can slip. Cord-face ladder shoes are recommended for wet surfaces, rubber or neoprene ladder shoes for smooth dry floor surfaces, and steel spikes for ice or snow. Be careful if you use an extension ladder on oily, metal, or concrete surfaces. Place the ladder securely and tie it off to prevent it from slipping.

## Slide 11: Self-supporting ladders
Standard stepladder
  Flat steps, hinged back
  Use on firm level footing
  Metal, wood, fiberglass
  One worker
  Metal spreader or locking arms
  No work from top step
  20 feet maximum length
Notes: The standard stepladder, a general purpose ladder, has flat steps and a hinged back. It is self-supporting and nonadjustable. An industrial model, designed for heavy service demands, has stronger legs, heavy-duty flat steps, and knee braces that increase rigidity and durability.
Standard stepladders should be used only on surfaces that offer firm, level footing such as floors, platforms, and slabs. They are available in metal, wood, or reinforced fiberglass, and are intended to support only one worker at a time. Remember not to stand on or work from the top step. The ladders must have a metal spreader or locking arms. They can’t be longer than 20 feet, measured along the front edge of the side rails.

## Slide 12: Self-supporting ladders
Two-way stepladder
  Similar to standard
  Steps on both sides
  Two people
  < 20 feet
Notes: The two-way stepladder is similar to the industrial standard stepladder; however, each side of this ladder has a set of steps. The extra set of steps offers convenience and versatility: One person can work from either side or two people can work from the ladder at the same time — one on each side.

## Slide 14: Self-supporting ladders
Platform ladder
  Special purpose
  < 20 feet to platform
  Stable platform is highest working height
Notes: The platform ladder is a special-purpose ladder that has a large stable platform from which you can work at the highest standing level. The ladder’s length is determined by the length of the front edge of the side rail from the bottom of the ladder to the base of the platform. The length of a platform ladder can’t exceed 20 feet.

## Slide 15: Self-supporting ladders
Orchard ladder
  Special purpose for pruning/harvest use
  One person
  16 feet maximum
  Wood, metal, fiberglass
  DO NOT stand on top step
Notes: The orchard ladder is a special-purpose ladder for pruning and harvest work. It has a flared base and a single back leg that offers support on soft, uneven ground. A doubled base on the rails controls penetration in soft soil.
Spreaders, locking devices, sharp points, or safety shoes are not required on orchard ladders.
Orchard ladders are intended for use by only one person at a time and can’t be longer than 16 feet. Metal and reinforced fiberglass versions are available.
A more rigid orchard ladder, the so-called double base version, incorporates a triangular box brace with stub rails attached to the bottom step. The ladder is available in wood or with a combination wood or fiberglass rail and metal step. Maximum length is 16 feet and it is intended for use by one person.
You should not stand on or work from the top step of an orchard ladder.

## Slide 16: Self-supporting ladders
Trestle ladder
  Two sections, hinged
  Used in pairs to support planks or staging
  Angle of spread = 5.5 inches per foot of length
  < 20 feet
  Spreaders required
Notes: A trestle ladder is a self-supporting portable ladder that has two sections hinged at the top, forming equal angles with the base. A variation of the trestle ladder, the extension trestle ladder, includes a vertically adjustable single ladder that can be locked in place. (The single extension section must lap at least three feet into the base section.) Trestle ladders are used in pairs to support planks or staging. The rungs are not intended to be used as steps.
The angle of spread between open front and back legs must be 51/2 inches per foot of length. The length can’t be more than 20 feet, measured along the front edge of the side rails. Rails must be beveled at the top and have metal hinges to prevent spreading. Metal spreaders or locking devices are required to keep the rails in place.

## Slide 18: Selecting Ladders
Other ladders for special needs
  platform
  trolley
  side-rolling
  shaft
  Manhole
Choose the right ladder for the job!
Notes: Ladders come in different types because workers who use them have different needs. In the previous section, we identified major types of portable ladders and the tasks for which they are appropriate. However, we omitted many special-purpose ladders, which are usually variations of general-purpose ladders that are designed to meet a special need.
Examples include platform, trolley, side-rolling, shaft, and manhole ladders. The important point: You are likely to save time and energy and reduce your risk of injury if you choose the right ladder for your task or job.

## Slide 20: Selecting Ladders
Example 1
A medium-duty, four-legged stepladder is designed for use on firm, level footing. If you use it frequently on soft, uneven ground — typical in orchard work — it will eventually twist and fail to support a load. You risk becoming a victim of the most common ladder accident — a ladder that tips over.
Example 2
An orchard ladder lacks locking arms or spreaders. When used on a firm, smooth footing, the tripod leg or pole tends to creep forward. The result is another common accident scenario — the ladder is likely to collapse.
Notes: These two examples illustrate what can happen when a ladder is used in an inappropriate manner.

## Slide 21: Using Ladders
Accidents happen:
  fail to inspect
  place inappropriately
  ignore safe practices when climbing
Notes: Ladders are easier and safer to use when you match them with the appropriate task. Still, most portable-ladder accidents happen when workers do one or more of the following: fail to inspect ladders regularly, place ladders inappropriately, or ignore safe practices when climbing or descending. The guidelines below address each of these issues.

## Slide 22: Using Ladders
Beginning a job
  select appropriate ladder for task
  inspect ladder –
    clean
    undamaged
Notes: At the beginning of each job
Select the appropriate ladder for your task or job.
Inspect the ladder before you use it. Make sure it’s in sound condition — clean and undamaged.

## Slide 23: Using Ladders
Placing a ladder
  near work
  proper angle
    extend ¼ the ladder length
    minimum slope 50 degrees
  solid rest across openings
  protect base from bumps
  orchard ladder pole on ground
Avoid...
  placing ladder in front of unlocked/unguarded door
  placing ladder on boxes, table, trucks or other movable objects
Notes: Placing a ladder
Move the ladder near the work you’re doing.
Angle the ladder properly. The base should extend not less than one-fourth the ladder’s length. The minimum slope should be 50 degrees.
Place a solid rest for the rail tops across window openings.
Protect the base of a tall, occupied ladder if it could be struck by vehicles or pedestrians.
Make sure the leg or pole of an orchard ladder doesn’t rest on a limb or in the crotch of a tree.
Avoid
Placing a ladder in front of an unlocked, unguarded door.
Placing a ladder on boxes, tables, trucks, or other moveable objects.

## Slide 24: What’s Wrong?
Notes: Improper practice: Improper placement angle of ladder; less than 4 to 1 ratio (height of ladder to horizontal distance out at base of ladder).

## Slide 25: Using Ladders
Securing a ladder
  nail/lash in place
  extend at least 36 inches above access area
Avoid
  exposed areas during storm or wind
  ladders covered with ice or snow
  using ladder if stairway can be used instead
Notes: Securing a ladder
Nail or lash a ladder in place if it will be used repeatedly in the same spot.
Select a ladder that will extend at least 36 inches above the access area it’s serving.
Avoid
Working on ladders in exposed areas during a severe storm or strong wind.
Working on ladders covered with ice or snow.
Using a portable ladder if an approved stairway could be used instead.

## Slide 27: Using Ladders
Ascending and descending
  face the ladder
  grasp rails with both hands
  raise/lower heavy loads with hand line or hoist
  attach light tools to ladder or person
Avoid
  sliding down ladder
  climbing with slippery hands/shoes
  using hands to carry items
  carrying awkward loads
Notes: Ascending and descending
Face the ladder at all times.
Grasp the side rails with both hands; you have a better chance of avoiding a fall if a rung or step fails.
Raise and lower heavy, awkward loads with a hand line or hoist.
Attach light, compact tools or materials to the ladder or to yourself.
Avoid
Sliding down the ladder.
Climbing when your hands or shoes are slippery
Using your hands for carrying items.
Carrying awkward loads when ascending or descending a ladder.

## Slide 29: Using Ladders
Securing equipment
  use strong bail hook on picker bucket
  when not using limb hook, secure it to ladder or nearby limb
Avoid
  placing tools/materials on ladder if they could fall off
Notes: Securing equipment
Use a strong bail hook on a picker bucket.
When you are not using a limb hook, secure it firmly to the ladder or to an adjoining limb.
Avoid
Placing tools or materials on a ladder if they could fall off.

## Slide 30
Notes: Improper practice: Improper use of step ladder for access.

## Slide 31: Using Ladders
Metal ladders
  skid resistant surface on steps, rungs
    corrugated
    knurled
    dimpled
    coated
  “WARNING — Do Not Use Around Energized Electrical Equipment.”
Avoid
  using ladders with conductive rails near exposed, energized equipment
Notes: Metal ladders
Make sure steps and rungs have a skid-resistant surface that minimizes the risk of slipping.
(“Skid resistant” means corrugated, knurled, dimpled, or coated with skid-resistant material.)
Permanently mark with the words, “WARNING — Do Not Use Around Energized Electrical Equipment.”
Avoid
Using any ladder with conductive side rails near exposed, energized equipment.

## Slide 32
Notes: Properly secured portable ladder extending 36 inches above landing.

## Slide 33: Using Ladders
Precautions
  both feet firmly on rungs and steps
  one person only on standard ladders
  inspect ladder that has collapsed, tipped, or exposed to harsh chemicals
  extend extension ladder > 36 inches above access
  keep area around ladder free of debris
  keep load on ladder (including worker) below maximum load capacity
Notes: Precautions
Place both feet firmly on the ladder rungs and steps.
Make sure only one person stands on, or works from, a standard ladder. (Use a scaffold or a second ladder if two or more people are doing the same task.)
Immediately inspect any ladder that has collapsed, tipped over, or been exposed to oil or grease. Clean and repair the ladder if necessary.
Remove defective ladders from service. Tag or mark defective ladders with the words: “Dangerous, Do Not Use.”
Make sure an extension ladder extends at least 36 inches above an access landing.
Keep the area around the top and bottom of a ladder free of debris.
Keep the load on the ladder (including yourself) below its maximum load capacity.

## Slide 34: Using Ladders
Do NOT
  paint ladders; use transparent preservative
  use ladders with broken, patched, oily parts
  use ladder as guy, brace, or skid
  stand or sit on top 2 steps of stepladder
  reach out over side rails, lean, turn
  use self-supporting ladders without spreader or locking device
  load ladder beyond maximum load capacity
Notes: Don’t...
Paint ladders. Paint conceals defects. Use transparent preservatives instead.
Use ladders with broken, patched, oily, or cracked rails, rungs, or steps.
Reach out over the side rails, lean, or turn excessively on a ladder.
Use a ladder as guy, brace, or skid.
Stand or sit on the top two steps of a stepladder.
Use a self-supporting ladder without first opening it up and securing the metal spreader or locking device.
Load a ladder beyond its maximum load capacity.

## Slide 35: Transporting Ladders
Hand carry
  elevate front end
Vehicle transport
  parallel to bed
  don’t toss or throw into bed
  support ladder so it won’t bend or sag
  secure ladder to vehicle
  drive slowly over rough terrain
Notes: Some ladders are easier to move than others. Here are a few guidelines to help you protect ladders and the people who use them.
When you hand-carry a ladder, keep the front end elevated, especially around blind corners, in aisles, and through doorways. You’ll reduce the chance of striking another person with the front of the ladder.
When you transport a ladder in a truck or trailer, place it parallel to the bed. Avoid tossing, throwing, or dropping it in the bed.
If you transport a long ladder on a short truck bed over long distances, support the ladder so it won’t sag or bend.
Drive slowly over rough terrain. Tie the ladder securely to eliminate nicking, gouging, chafing, and road shock.

## Slide 36: Storing Ladders
Well ventilated area
Limit exposure to moisture/excessive heat
Store straight/extension ladder on flat racks or wall brackets – no sagging
Store stepladder and orchard ladder vertically in closed position
Store promptly after use
Limit exposure of wood and fiberglass to moisture and sunlight
Notes: Storing Ladders
Another way to prolong a ladder’s life is to store it properly. Some useful storage tips:
The storage area should be well ventilated.
Wood ladders shouldn’t be exposed to moisture or excessive heat. Avoid storing ladders near stoves, steam pipes, or radiators.
Store straight or extension ladders in flat racks or on wall brackets. Make sure there are enough brackets to support the ladder so that it doesn’t sag. If the ladder rails have a lateral curve, the wall brackets should match the curve.
Store stepladders and orchard ladders vertically, in a closed position, to reduce the risk of sagging or twisting. Secure stored ladders so that they won’t tip over if they are struck.
Store ladders, especially wood ladders, promptly after using them. Exposure to moisture and sun will shorten the life of wood and fiberglass ladders.

## Slide 37: Maintaining Ladders
Neglected ladders quickly become unsafe ladders
Maintenance – regular inspection, tighten step bolts and fastenings
Do not paint wooden ladder – hides defects
Notes: Maintaining and Repairing Ladders
Neglected ladders quickly become unsafe ladders. Step bolts slacken, step sockets and other joints work loose, hole sizes increase — eventually the ladder becomes twisted and unstable.
Periodic maintenance extends a ladder’s life and saves replacement costs. Maintenance includes regular inspection of the ladder, repairing damage and tightening step bolts and other fastenings.
Don’t paint a wood ladder — paint conceals defects.

## Slide 38: Repairing Ladders
Wooden ladder: replace lower steps when ¼ of step is worn away
Non-skid surface reduces wear
Don’t use cleats to repair rung ladder
Do not paint wooden ladder
Stock repair parts – ladder bolts, lower steps, related hardware
Notes: Maintaining and Repairing Ladders
Replace lower steps on wooden ladders when one-fourth of the step surface is worn away. Typically, the center of a step receives the most wear. (Mineral abrasive or other skid-resistant material reduces wear.)
Don’t use cleats to repair rung ladders.
Consider stocking repair parts if you use different types of ladders. Typical parts include ladder bolts, related hardware, and lower steps or rungs (which wear out faster than upper steps or rungs).

## Slide 39: Improve Slip Resistance
Cloth-backed mineral abrasive
Anti-slip abrasive surfacer
Coarse-ground walnut shells
Sand
Re-dimpling (for metal ladders)
Notes: Improving Slip Resistance
Slip-resistant materials are often used on industrial-ladder treads. Notable is the anti-slip treatment on metal platform ladders used in file and parts rooms, tool cribs, and frozen-food lockers. The obvious benefit of slip-resistant material is that it reduces fall risks when a worker is climbing or descending. Common slip-resistant materials you can apply:
Cloth-backed mineral abrasive: Made in strips, panels, and large sheets. An adhesive-backed, pressure-sensitive type and a plain type requiring cement, are available. Both types can be applied to any clean, dry surface. Use an edge sealing (beading) compound over the application to make it last longer.
Anti-slip abrasive surfacer: A mastic-type compound containing mineral abrasive that is troweled on in a thin coat.
Coarse-ground walnut shells: A wall-texturing material used by decorators, available in most paint stores. Mixed into spar varnish, about one part shells to three or four parts varnish, it makes a good slip-resistant ladder tread surface. When applying the material to metal steps, use a damp-proof primer before applying the varnish.
Sand: When properly applied, sand can enhance slip resistance. The recommended procedure is to varnish steps or rungs, then sift dry sand onto the wet varnished surface. After allowing ample drying time, shake off surplus sand. (You can apply a thin coat of spar varnish over the sand to strengthen the bond.)
Re-dimpling: Metal ladder treads that have round dimples worn smooth can be re-dimpled with a tapered punch driven upward in same line as the original dimpling.

## Slide 40: Checklists
Available from EH&S
Ladder hazards
Ladder training

## Slide 41: Definitions
Check
Cleat
Competent person
Decay
Extension ladder
Extension trestle ladder
Fastening
Ladder
Platform ladder
Rungs
Sectional ladder
Single (or straight) ladder
Special-purpose ladder
Stepladder
Steps
Tread
Tread width
Trestle ladder
Notes: Check A lengthwise separation of the wood that occurs across the rings of annual growth.
Cleat A rectangular ladder crosspiece placed on edge, upon which a person may step while ascending or descending.
Competent person A person who can identify existing and predictable hazards in the work environment and who has authorization to take prompt measures to eliminate the hazards.
Decay Disintegration due to action of wood-destroying fungi. Also known as dote or rot.
Extension ladder A non-self-supporting portable ladder that is adjustable in length. It consists of two or more sections in guides or brackets that permit length adjustment. Length is designated by the sum of the lengths of each section, measured along the side rails.
Extension trestle ladder A self-supporting portable ladder that is adjustable in length, consisting of a trestle ladder base and a vertically adjustable single ladder with means for locking the ladders together. Length is designated by the length of the trestle ladder base.
Fastening A device that attaches a ladder to a structure, building, or equipment.
Ladder An appliance usually consisting of two side rails joined at regular intervals by crosspieces called steps, rungs, or cleats on which a person steps when ascending or descending.
Platform ladder A self-supporting ladder of fixed size with a platform at the working level.
Rungs Ladder crosspieces of circular or oval cross-section on which a person steps when ascending or descending.
Sectional ladder A non-self-supporting portable ladder, nonadjustable in length, consisting of two or more sections that function as a single ladder. Its length is designated by the overall length of the assembled sections.
Single (or straight) ladder A single section non-self-supporting portable ladder, nonadjustable in length. Its length is measured along a side rail. Special-purpose ladder A general-purpose portable ladder with modified features for specific uses.
Stepladder A self-supporting portable ladder, nonadjustable in length that has flat steps and a hinged back. Length is measured along the front edge of a side rail.
Steps The flat crosspieces of a ladder on which a person steps when ascending or descending.
Tread The horizontal member of a step.
Tread width The horizontal distance from front to back of the tread, including nosing.
Trestle ladder A self-supporting portable ladder, nonadjustable in length, that consists of two sections hinged at the top to form equal angles with the base. Length is measured along the front edge of a side rail.